Analog Integrated Circuit Design

HW#2

Making use of both HSPICE and a 0.18(m CMOS technology, simulate the following circuit.

|  | L(µm) W(µm) 0.18 4 M1, M2 0.18 45 M3, M6 0.18 30 M4, M5 |
| --- | --- |

, ,

- In order to set the dc voltage of the output of the amplifier to 0.9 V, find a proper dc voltage for the input signal.

- Why is  too much sensitive to ?

- Making use of ".OP", report the following parameters for each transistor.

ID, gm, VDS, VGS, VDsat, Vth, rds, Cgs, Cgd, Cdb, Csb

- Making use of ".Tran", find the amplitude of the input sinusoidal signal so that .

- What is the voltage gain of the amplifier at ?

- Making use of ".AC", plot the amplitude frequency response of the amplifier and determine the following parameters.

  - (dc voltage gain of the amplifier)

  - (voltage gain of the amplifier at )

  - (-3 dB cut-off frequency)

  - (unity gain frequency)

- Is the following relation is correct?

- Conclude about the capabilities of ".OP", ".Tran", and ".AC"