## Slide 1: VARSYS Module of WASP-IV
Mladen Zeljko, Ph.D.
Head of Energy Generation and Conversion Department
Energy Institute “Hrvoje Požar”
Tel: +385 1 6326186 Fax: +385 1 6040599
E-mail: mzeljko@eihp.hr
www.eihp.hr

## Slide 2: Objectives of the Variable System Module (VARSYS)
Taking into account cost and operating parameters of the power plants to be considered as expansion candidates
Transferring processed data to other modules
Data input is very similar to the one described in explanation of the FIXSYS module

## Slide 3: Thermal Plant Data Requirements in VARSYS
Thermal plant data are entered and edited in the same way as in FIXSYS
The maximum number of different expansion candidates (unit types) is 12, unless pumped storage plants are defined (in that case 11)
The number and type of group limitations has to be consistent with the definitions in FIXSYS; redefinition of group limitations is not possible in VARSYS

## Slide 4: Hydro Plant Data Requirements in VARSYS
As with thermal plants, hydro plant data are also entered in the same way as in FIXSYS
Up to 30 projects can be defined within each hydro plant category (two composite hydro plants, pumped storage projects)
For each hydro project, the first year in which the project is available has to be entered (unlike FIXSYS)

## Slide 5: Entering Hydro Projects in VARSYS
Since hydro projects compete against each other in the order they are entered, the criteria of economics and availability should be considered simultaneously
Example:
Assume that the projects were entered in the following order: A1 A2 A3 B1 B2; the projects would then compete in the following manner:
  A1 competes against B1  A1 is chosen
  A2 competes against B1  A2 is chosen
  A3 competes against B1  A3 is chosen
  B1 is chosen
  B2 is chosen
Therefore, it would be better to use the following entering order: A1 A2 A3 B2 B1

## Slide 6: Main Outputs Produced in VARSYS
Module output is generated and viewed in the same way as in FIXSYS (filename: varsys.rep)
VARSYS determines the economic loading order of candidate thermal unit types, based on total full load unit generation costs
Operating characteristics (base and peaking capacity, peaking energy, peaking hours, operating mode) of individual hydro projects are calculated for each period and hydrocondition
Characteristics of composite hydro plants are generated by combining the individual parameters of all hydro projects of the same type

## Slide 7: Checking printout of FIXSYS and VARSYS
After execution each of two modules the printouts should be checked with great care. Be shure that reported numbers are those intended by the user
Possible inconsistencies between FIXSYS and LOADSY, or between FIXSYS and VARSYS should be checked before going to the CONGEN module
Some types of error (if exsist) will be printed in the printout files. If it will happen look the list of errors for each module in the Manual