## Slide 1: FIXSYS Module of WASP-IV
Mladen Zeljko, Ph.D.
Head of Energy Generation and Conversion Department
Energy Institute “Hrvoje Požar”
Tel: +385 1 6326186 Fax: +385 1 6040599
E-mail: mzeljko@eihp.hr
www.eihp.hr

## Slide 2: INPUT/OUTPUT files of FIXSYS
Input data file, fixsys.dat, is created from data provided by the user
FIXSYS produces the following files: fixplant.bin, fixsysgl.wrk, fixsysgl.dbg and fixsys.rep
All files can be accessed within the C\WASP-IV\Study_n\Case_m directory once the FIXSYS module has been executed
If input data are entered or modified manually, they should be prepared exactly according to the format described in the User’s Manual

## Slide 3: Objectives of the Fixed System Module (FIXSYS)
Taking into account cost and operating parameters of existing power generating units
Considering firmly scheduled unit additions and retirements
Transferring processed data to other modules

## Slide 4: FIXSYS Inputs
Names and short descriptions of up to 10 different thermal fuel types
Names and descriptions of up to 2 hydro power plant types
Names and related parameters for up to 88-NTHPLVARSYS thermal power plants
Names and related parameters for individual hydro projects within the two hydro plant types and/or pumped storage projects (max. 30 projects in each category)
Fixed additions and retirements of the existing generating system
Group limitations and pollutant emission parameters (new features of WASP-IV)

## Slide 5: Thermal Plant Data Requirements in FIXSYS
Thermal plants are easily added to or removed from the list by clicking the Add Plant or Remove Plant button
Required thermal plants parameters include:
  Plant name (up to 4 chars)
  Number of identical units at start of the study
  Minimum and maximum operating capacities
  Heat rates (at min. level and avg. incremental)
  Fuel type (from a pre-defined fuel list)
  Fuel cost (domestic and foreign)
  Fixed and variable O&M cost
  Forced outage rate
  Spinning reserve as percentage of unit capacity
  Days of required maintenance and maintenance class size
  Heat value of the fuel and pollutant emission factors

## Slide 6: Thermal Plant Data Requirements in FIXSYS (cont’d)
All predetermined retirements and additions should be entered into the table which appears after clicking the Additions/Retirements of Thermal Plants button
The number of units which are to be added/retired is entered into the appropriate cell for the plant and the year considered
A correct sign should be put in front of the number (+ for additions, – for retirements)

## Slide 7: Thermal Plant Data Requirements in FIXSYS - Emissions
In case emission calculations are to be performed, the appropriate parameters should be entered for the considered thermal plant (fuel heat value, emission factors)
In the window which is opened after pressing the Emissions button, the user can define groups of plants which produce a particular pollutant

## Slide 8: Thermal Plant Data Requirements in FIXSYS - Group Limits
In order to specify group limitations for thermal plants, the number of group limits (up to 5) should be entered first; after a non-zero number is entered, clicking the Group Limits button opens the data input window
Each group limit can be of one of five predefined types: fuel quantity, pollutant 1, pollutant 2, fuel heat value and electricity generation
All limits are on annual basis!!
With this feature it is possible to simulate various real-life constraints

## Slide 9: Hydro Plant Data Requirements in FIXSYS
Individual hydro projects are integrated into max. two hydro plant groups, which can represent different hydro categories (e.g. run-of-river and storage plants)
Input window for data related to hydro projects is shown after pressing the Hydro/Pump Storage Plants button

## Slide 10: Hydro Plant Data Requirements in FIXSYS (cont’d)
Hydro plants can also be easily added or removed by using Add Plant or Remove Plant button
O&M costs are entered at the group level
Required data for individual hydro projects include:
  Hydro plant type
  Installed capacity
  Reservoir capacity
  Year of operation
  Data specified for each period and hydrocondition:
    Inflow energy
    Minimum generation (due to downstream water commitments)
    Average capacity

## Slide 11: Hydro Plant Data Requirements in FIXSYS - Pumped Storage Plants
Representation of pumped storage hydro plants is a new feature of WASP-IV
Pumped storage plants are added and removed in the same manner as hydro projects
Required data for pumped storage plants include:
  Installed capacity
  Year of operation
  Fixed O&M cost
  Cycle efficiency
  Data specified for each period:
    Pumping capacity
    Generating capacity
    Maximum feasible energy generation

## Slide 12: Main Outputs Produced in FIXSYS
FIXSYS Module outputs are stored in the file named fixsys.rep after the module has been executed; the file can be accessed directly from WASP-IV user interface and viewed with WordPad
FIXSYS gives data for the economic loading order of existing thermal units, based on maximum load generation costs
Operating characteristics of individual hydro projects (base and peaking capacity, peaking energy, peaking hours, operating mode) are calculated for each period and hydrocondition
Composite hydro plants (by type) are generated by summing up the parameters of individual projects