## Slide 1: Remersim module of WASP-IV
Mladen Zeljko, Ph.D.
Head of Energy Generation and Conversion Dept.
Energy Institute Hrvoje Pozar
Savska cesta 163
10 000 Zagreb, Croatia
phone: +385 1 6326186
e-mail: mzeljko@eihp.hr

## Slide 2: DYNPRO Produces a File Called EXPANREP Containing One Configuration Per Year for the Optimal Solution
CONGEN
EXPANALT
MERSIM
DYNPRO
EXPANREP
REPROBAT
SIMULNEW
REPORT ON
FINAL SOLUTION
SIMULOLD
INPUT
DATA
REMERSIM
SIMULNEW
Phase 1 = Looking for Optimal Solution
Phase 2 = Reporting on Optimal Solution

## Slide 3: Reporting on the Optimal Solution
DYNPRO
EXPANREP
REPROBAT
REPORT ON
FINAL SOLUTION
REMERSIM
SIMULNEW
30
30
Phase 2 = Reporting on the Optimal Solution

## Slide 4: REMERSIM Module of WASP-IV
The execution of REMERSIM is the same as MERSIM, except that different input files are used and more detailed output is produced.
REMERSIM is Executed to
Produce Detailed Simulation
Results for Reviewing and as
input to REPORBAT

## Slide 5: REMERSIM Input Data
KEY INPUTS:
In each year, the level of output specified must be either Intermediate or Maximum if the REMERSIM run is to be followed by a REPROBAT run.
The rate of fuel consumption and level of fuel stocks can be specified for each thermal plant type.

## Slide 6: Fuel consumption and fuel stock
Fuel consumption (Ton/GWh)
Heat rate (kcal/kWh)/Calorific value (kcal/kg)
= kg/kWh =Ton/MWh = 1000 Ton/GWh
Fuel stock at the beginning of the year (Tons)
- Consumption of fuel in that year (Tons)
= Fuel stock at the end of the year (Tons)

## Slide 7: REMERSIM Output
KEY OUTPUTS:
Operational results of the simulation (including pumped-storage operation if exists) for each period, hydro condition and year of the study
Detailed results of group
limitations, including loading
order and operational details for
the initial stage and the final
stage after the group limitations
are applied.