## Slide 1: CONGEN Module of WASP-IV
Mladen Zeljko, Ph.D.
Head of Energy Generation and Conversion Department
Energy Institute “Hrvoje Požar”
Tel: +385 1 6326186 Fax: +385 1 6040599
E-mail: mzeljko@eihp.hr
www.eihp.hr

## Slide 2: CONGEN: THE CONFIGURATION GENERATOR
What is a system configuration?
A configuration is a shorthand representation of new
capacity additions:
Year LIG3 LIG6 COL5 CC5 NU10 HY1 HY2
2010 0 1 0 2 0 0 1

## Slide 3: CONGEN’S MAIN FUNCTION
  To generate a list of configurations that can meet future electricity demand, while satisfying certain constraints:
    Maximum number of candidate technologies (14)
    Minimum installation requirements
    Tunnel width
    Reserve margin
    Hydro availability (critical hydro condition)

## Slide 4: CONGEN’S DATA REQUIREMENTS
Output files from LOADSY, FIXSYS, and VARSYS
Minimum and maximum reserve margin:
  % of peak load in the critical period,
  may change during the study period.
Hydro condition for which the critical period and reserve margins are calculated (usually the dry condition).

## Slide 5: CONGEN DATA REQUIREMENTS
Minimum number of new units that must be in operation.
Maximum number of additional units that can be added by the program (tunnel width).
Example:
2020 COAL LIGN CC NUC HYD1 HYD2
Minimum 0 1 2 0 1 0
Tunnel Width 1 2 2 1 2 1

## Slide 6: CONGEN DATA REQUIREMENTS (cont.)
The tunnel widths define the maximum possible number of configurations available in a year.
  (e.g., 2 X 3 X 3 X 2 X 3 X 2 = 216 )
Number of configurations:
WASP III Plus: 300 per year, 3000 over the study period
WASP IV: 500 per year, 5000 over the study period

## Slide 7: WASP IV MODIFICATIONS
New order of candidate projects:
(a) Case with candidate pumped-storage projects:
Up to 11 thermal technologies
Up to 2
hydro
types
Pumped
-storage
type
(b) Case without candidate pumped-storage projects:
Up to 12 thermal technologies
Up to 2
hydro
types

## Slide 8: CONGEN INPUT FILE
EXAMPLE Input File:
11111111112222222222333333333344444444445555555555666666666677777777778
12345678901234567890123456789012345678901234567890123456789012345678901234567890
CASE 96: CASE STUDY FOR THE WASP-IV USER'S MANUAL 1
4
10.0 35.0
2
0 0 0 0 0 1 0 {4 thermal plants, 2 hydro types, 1 P-S type}
3
0 0 0 0 0 0 0 {4 thermal plants, 2 hydro types, 1 P-S type}
1 (END OF 1985)
2
0 0 0 0 1 1 0 {4 thermal plants, 2 hydro types, 1 P-S type}
1 (END OF 1986)

## Slide 9: CONGEN OUTPUT REPORT (Cover Page)
WASP COMPUTER PROGRAM PACKAGE
CONGEN MODULE
CASE STUDY
CASE 96: CASE STUDY FOR THE WASP-IV USER'S MANUAL
**************************************
* *
* LIST OF VAR. EXPAN. CANDIDATES *
* *
**************************************
* *
* THERMAL PLANTS *
* *
* SEQU.NUMBER NAME *
* *
* 1 VCOA *
* 2 VFOL *
* 3 VNUC *
* 4 V-GT *
**************************************
* *
* HYDROELECTRIC PLANTS *
* *
* SEQU.NUMBER NAME *
* *
* 5 SHTS *
* 6 LOTS *
**************************************
* *
* PUMPED STORAGE PLANTS *
* *
* SEQU.NUMBER NAME *
* *
* 7 PUMP *
**************************************

## Slide 10: CONGEN OUTPUT REPORT (Fixed Expansion Plan)
CONDITIONS GOVERNING ALTERNATIVE GENERATION * * * * * * YEAR 1985 * * * * * * * * * *
MINIMUM REQUIRED OF EACH ALTERNATIVE 0 0 0 0 0 1 0
MAXIMUM ADDITIONAL EACH ALTERNATIVE 0 0 0 0 0 0 0
RESERVE RANGE PERMITTED IN CRITICAL PERIOD (%) 10.00 35.00
CALCULATION OF CRITICAL PERIOD IS BASED ON HYDRO CONDITION 1
TOTAL CAPAC. PERIOD
PER IN FIXSYS --- THERMAL PUMPING HYDRO 1 HYDRO 2 --- PEAK LOAD
1 5930.8 3802.0 300.0 378.8 1450.0 4500.0
2 5960.4 3802.0 300.0 398.4 1460.0 4250.0
3 6012.2 3802.0 300.0 420.2 1490.0 4500.0
4 6021.2 3802.0 300.0 399.2 1520.0 5000.0
CRITICAL PERIOD IS 4
CAPACITY RANGE IN CRITICAL PERIOD IS 5500.0 6750.0
COMMITTED CAPACITY SPECIFIED IN CRIT PERIOD 6281.2
MINIMUM NUMBER OF FOURIER COEFF. CORRESPONDING TO MAXIMUM RESERVE MARGIN IN CRIT PER IS 3
STATE IC CAP ACCEPTED CONFIGURATION
1 1 6281. 0 0 0 0 0 1 0
CONFIGURATIONS THIS YEAR 1
CONFIGURATIONS THROUGH THIS YEAR 1
* * * * * * * * * * * * * * * * * * * END OF YEAR 1985 * * * * * * * * *