## Slide 1: Pumped-Storage Hydro Representation in WASP-IV
Mladen Zeljko, Ph.D.
Head of Energy Generation and Conversion Department
Energy Institute “Hrvoje Požar”
Tel: +385 1 6326186 Fax: +385 1 6040599
E-mail: mzeljko@eihp.hr
www.eihp.hr

## Slide 2: Pumped-Storage Hydro Power Plants
Pumped-storage plants save fuel cost by off-loading high cost peaking thermal units with hydro energy pumped to reservoir during low demand periods (night, weekend) using cost-efficient units
Pump storage plants are limited both in capacity and energy

## Slide 3: Conventional Hydro and P-S Plants in WASP-IV
Composite hydro plants HYDA & HYDB are combined into a single composite plant
Former composite hydro plant HYDA represents the generation side of pumped storage plant
HYDA + HYDB ------> HYDR
HYDA ------> PUMP
If P-S plant is not active, composite hydro plants HYDA and HYDB are treated as in WASP III-plus

## Slide 4: Pumped-Storage Hydro Power Plants
Characteristics:
  Pumping capacity
  Generation capacity
  Storage capacity
  Pumping efficiency
  Generating efficiency
  Cycle efficiency
  O&M cost
Economic evaluation depends on:
  Characteristics of LDC
  Composition of the generating system
  Reliability of each unit
  Running cost of units (fuel and variable O&M)

## Slide 5: Pumped-Storage Plants Operation
For each block of each thermal plant j, the program computes:
  The energy Egj that can be replaced by the generation of the P-S plant
  The energy Epj that is available for pumping
Egj =  Epj
In a step-by-step procedure, pumping from the bottom and generating from the top of L.O., the largest amount of energy available for P-S operation is determined

## Slide 6: Pumped-Storage Plants Operation
Mode 1: Compulsory Operation
The P-S plant is dispatched as the last plant in the L.O. and its generating capacity is used for peaking service
Pumping is assigned to the lowest operation cost thermal units
This mode may be uneconomical, if it requires additional thermal generation for pumping duty without reducing the thermal generation

## Slide 7: Pumped-Storage Plants Operation
Mode 2: Economic Operation
Economic operation is only possible when sufficient pumping energy is available and cost of pumping water into reservoir is cheaper than the cost of thermal generation replaced by P-S operation
Cpi <  Cgj
where
  Cpi : Operating cost of thermal unit i that is used for pumping duty
  Cpj : Operating cost of thermal unit j that is off-loaded by the P-S plant
   : Efficiency of pumping cycle

## Slide 8: Limiting Conditions of P-S Operation
The P-S operation cycle is continued until one of the following conditions is reached:
Minimum P-S operation : once available energy is not sufficient for minimum (compulsory) P-S operation.
Economic : when operation is not economic, the P-S dispatch stops.
Cycle generation capability exhausted (pond cycle) : once the P-S plant has been utilized to the extent of the specified pond (maximum) capacity (GWh/cycle)

## Slide 9: Pumped Storage Plant Data Requirements in FIXSYS and VARSYS
Pumped Storage Plants window is accessed by clicking the Pump Storage Plant button in Hydro Plants window of FIXSYS and VARSYS modules
Individual projects can easily be added or removed by using Add Plant or Remove Plant button
Required data for pumped storage plants include:
  Installed capacity
  Year of operation
  Fixed O&M cost
  Cycle efficiency
  Data specified for each period:
    Pumping capacity
    Generating capacity
    Maximum feasible energy generation

## Slide 10: Drawbacks of P-S Operation in WASP-IV
The cycling operation of the P-S units (daily or weekly) is not taken into account
No possibility to use the available energy for pumping in one period in a subsequent period
More than one P-S plants are treated as one composite P-S plant

## Slide 11: Composite Pump – Storage Plant
P = Composite P-S plant pumping capacity (MW)
G = Composite P-S plant generating capacity (MW)
E = Composite P-S plant storage capacity (GWh)
np = Composite P-S plant pumping efficiency (%)
ng = Composite P-S plant generating efficiency (%)
n = Composite P-S plant cycle efficiency (%)