## Slide 1: DYNPRO Module of WASP-IV
Mladen Zeljko, Ph.D.
Head of Energy Generation and Conversion Department
Energy Institute “Hrvoje Požar”
Tel: +385 1 6326186 Fax: +385 1 6040599
E-mail: mzeljko@eihp.hr
www.eihp.hr

## Slide 2: Manual vs. Automated Generation Planning
Manual Generation Planning
involves very detailed analysis;
Combine discipline of reliability (LOLP evaluations), system production simulation and investment costing;
requires a great deal of manual intervention because there are many alternatives to examine;
in the middle 1960s optimization process was automated
Automated Generation Planning
several approaches to implement optimization procedure
one approach is an exact mathematical optimization procedure called “dynamic programming”
other approaches include linear programming, mixed integer-linear programming and several approximation techniques

## Slide 3: Dynamic Programming Optimization
Dynamic programming is an exact mathematical optimization procedure
The solution technique is recursive algorithm that proceeds backward from destination to source
Examination of traditional problem called “stagecoach problem” is application of dynamic programming
In “stagecoach problem” the person needs to travel between two cities and he can pass trough different cities by buying ticket with different price , and objective is to find least cost way for travel
objective is to compute the total cost of optimally traveling from any city that connect final destination city
“stagecoach problem” is similar to the generation planning problem - ticket is year of planning, ticket cost is analogous to annual cost (production and investment)

## Slide 4: Dynamic Programming Optimization
Types of problems it solves are called dynamic optimization problems, control problems, or optimization problem for multi-stage decision process.
Problems are characterized by the fact that decisions taken at present will affect the future decisions; hence the solution is a sequence of decision over the whole period, not just at the present time.
This type of problem occurs in virtually all engineering disciplines, as well as operations research, economics, physics, etc.
Because of the recursive nature of the problem, the approach is well suited for implementation on a computer.

## Slide 5: Dynamic Programming
DP was invented by Richard Bellman
It’s well suited for optimizing sequential decision processes such as electric power system generation expansion planning
That is the optimization technique used by WASP
It is based on Bellman’s Principle of Optimality

## Slide 6: Bellman’s Principle of Optimality
Given an optimal* trajectory TAC from A to C, the portion TBC of that trajectory from any intermediate point B to point C must be the optimal trajectory from point B to C.
A
C
TAB
TBC
B
TAC
* What does optimal mean?

## Slide 7: Bellman’s Principle of Optimality
Proof: Given the optimal trajectory TAC = TABTBC from A to C, then according to Bellman’s principle, TBC is the optimal trajectory from B to C. Assume that some other trajectory tBC is the optimal trajectory from B to C. Then the trajectory TABtBC must be better than TAC . But this contra-dicts the original hypothesis that TAC is the best (optimal) trajectory from A to C. Ergo, tBC cannot be better than TBC TBC is the optimal trajectory from B to C.
A
B
C
TAB
TBC
tBC
TAC

## Slide 8: Dynamic Programming Optimization
The first step in applying the dynamic programming is to define the cost-objective criteria
  usually, a plan is selected that has the least cumulative present-worth cost over study period horizon
L(x) =[Cj - Sj + FCj + OMCj + ENSCj]

## Slide 9: Dynamic Programming Optimization
The second step in applying the dynamic programming method is the calculation of the stage cost
  compute annual production simulations of the power system for each possible alternative route trough the study years
  the next phase is to compute the investment costs and added to production costs

## Slide 10: Dynamic Programming Optimization
The final phase is dynamic programming phase in which the costs are interrogated during the optimal solution process
  The first step in solution procedure is to begin with final destination (last year of study) and proceed toward the starting year (first year of study)
  The next step is to continue building the decision tree back toward the starting point using dynamic programming procedure
  Dynamic programming process would lead to an optimal cumulative present worth cost

## Slide 11: DYNPRO Module of WASP-IV
Applying principles of DP To DYNPRO/WASP:
Stage -> Year
State -> Configuration
Quality -> Objective Function
Purpose: Find the BEST EXPANSION POLICY that satisfies desired RELIABILITY CRITERIA at MINIMUM COST.
INITIAL
CONDITION
STATE 1
STATE 2
STATE 4
STATE 7
STATE 6
STATE 3
STATE 5
STAGE 1
STAGE 2
STAGE 3
l(1)
l(2)

## Slide 12: DYNPRO Module of WASP-IV
L(x) = value of objective function
Cj = present worth of capital costs associated with the decisions between stage j – 1 and j
Oj = present worth of operating costs in stage j for the state associated with the decisions prior to stage j
Objective function in a simplified form:
INITIAL
CONDITION
STATE 1
STATE 2
STATE 4
STATE 7
STATE 6
STATE 3
STATE 5
STAGE 1
STAGE 2
STAGE 3
Retained
path
Discarded
path

## Slide 13: DYNPRO Module of WASP-IV
Let us consider state 3:
L1 = C(3-1) + I(1), L2 = C(3-2) + I(2), min. I(3) = L1
The path from state 2 to state 3 is discarded as being uneconomical and is not included in any further consideration of state 3
The same analysis is repeated for state 4 and only optimal decision is retained
INITIAL
CONDITION
STATE 1
STATE 2
STATE 4
STATE 7
STATE 6
STATE 3
STATE 5
STAGE 1
STAGE 2
STAGE 3
Retained
path
Discarded
path

## Slide 14: DYNPRO Module of WASP-IV
In the third stage one may proceed from states 3 to or 4 to states 5, 6 or 7 and the same logic is applied to this set of decisions
Optimal end of state and optimal trajectory can be determined by selecting the final objective function as:
I= Min [I(5), I(6), I(7)]
The optimal path is traced backward to the initial condition
INITIAL
CONDITION
STATE 1
STATE 2
STATE 4
STATE 7
STATE 6
STATE 3
STATE 5
STAGE 1
STAGE 2
STAGE 3
Retained
path
Discarded
path

## Slide 15: DYNPRO Module of WASP-IV
DYNPRO is based on information coming from:
VARSYS: Elements composing a state (configuration)
CONGEN: States of each stage
MERSIM: Elements defining quality:
- Operation costs
- Energy not served
DYNPRO: Elements defining quality:
- Reference years
- Capital costs
- Economic parameters
- Energy not served cost
- Mode of salvage value calculation
Elements influencing quality:
- Critical LOLP
- Limitation on number of plants to be built

## Slide 16: DYNPRO Module of WASP-IV
Utilizes dynamic programming optimization to determine the best expansion path for the system, based on previously derived operating costs along with input information on capital cost, ENS cost, and economic parameters and criteria

## Slide 17: DYNPRO Inputs
KEY INPUTS:
Local and foreign components of the investment costs
(overnight cost including interest during construction · IDC)
Economic lifetime of generating units
Construction lead times
Discount rates for capital and operating costs (local and foreign)
Fuel escalation rates
Critical Loss-of-Load-Probability (LOLP)
Energy-not-served (ENS) cost

## Slide 18: DYNPRO Output (dynpro1.rep)
REPORT:
Cover page
Input data
Objective functions of states
Trajectory path
Optimal solution
Optional: VARSYS input file and list of states considered in the run
Objective function:
Calculations are based on:
  Start of year capital costs
  Middle of year operating costs

## Slide 19: DYNPRO1.rep
SOLUTION # 1 VARIABLE ALTERNATIVES BY YEAR
YEAR------ PRESENT WORTH COST OF THE YEAR ( K$ )------ OBJ.FUN. LOLP VCOA VNUC HYD1
CONCST SALVAL OPCOST ENSCST TOTAL (CUMM.) % VFOL V-GT HYD2
- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
2016 115242 105764 474642 0 484120 13690766 .004 0- 15 0- 25 3+ 0-
2015 124462 104746 486617 0 506332 13206646 .002 0- 14 0- 25 3+ 0-
2014 333705 255137 498796 0 577365 12700314 .001 0- 13 0- 25 3+ 0-
2013 168525 117936 515607 1 566197 12122949 .016 0- 11 0- 22 3+ 0-
2012 156786 101180 528717 3 584326 11556752 .020 0- 10 0- 21 3+ 0-
2011 169329 99796 545794 1 615328 10972426 .011 0- 9 0- 21 3+ 0-
2010 300544 153573 552121 0 699092 10357098 .003 0- 8 0- 21 3+ 0-
2009 229276 109862 550374 1 669789 9658006 .008 0- 7 0- 17 3+ 0-
2008 213306 94944 555137 0 673499 8988217 .004 0- 6 0- 16 3+ 0-
2007 571912 221314 560499 0 911097 8314719 .003 0- 5 0- 16 3+ 0-
2006 368866 123790 580732 5 825812 7403622 .026 0- 3 0- 13 3+ 0-
2005 338854 110462 555929 12 784334 6577810 .043 0- 2 0- 10 3+ 0-
2004 0 0 567399 21 567420 5793476 .059 0- 2 0- 7 2 0-